## Slide 1: SCREW THREADS AND LOCKING DEVICES
This module is designed to develop your awareness and competence in thread forms and locking devices in accordance with your current training objectives set out in your ROA (record of achievement).
At the end of this input, the trainee will have an understanding of fixings, fasteners and any item with a thread and be able to identify it and satisfactorily complete a test of understanding as verification.

## Slide 2: SCREW THREADS AND LOCKING DEVICES
There are many standards for screw threads used on bolts and fastenings. They all have a specific formation and each is very different to the other..
butress
acme
PITCH
PITCH/2
SQUARE

## Slide 3: SCREW THREADS
There are several standards (British Standards) of thread available, on site you will usually see only three of these in use.
Unified Thread Form BS1580
Whitworth Thread Form BS 84
Metric Thread Form BS 3643
angle = 55º
angle = 60º
angle = 60º

## Slide 4: SCREW THREADS
There are several standards (British Standards) of thread available, on site you will usually see only three of these in use.
Unified Thread Form BS1580
Whitworth Thread Form BS 84
Metric BS 3643
Imperial
metric
BSW, BSF, UNC, UNF

## Slide 5: SCREW THREADS
There are several standards (British Standards) of thread available, on site you will usually see only three of these in use.
Unified Thread Form BS1580
Whitworth Thread Form BS 84
Metric BS 3643
British Association - BA
60º
55º
60º
47.5º

## Slide 6: SCREW THREAD TABLES
Imperial
metric

## Slide 7: SCREW THREAD MISMATCH

## Slide 8: SCREW THREAD MISMATCH
Correct thread
Mismatched thread
½” Whitworth+ ½” UNC

## Slide 9: FASTENERS AND LOCKING DEVICES - SCREWS
WOOD SCREWS
MACHINE SCREWS
SHEET METAL SCREWS
SELF DRILLING SCREWS

## Slide 10
FASTENERS AND LOCKING DEVICES – NUTS & BOLTS
HEXAGONAL BOLTS
CARRIAGE BOLTS
LAG BOLTS
SET SCREW

## Slide 11: ADDITIONAL TYPES OF FIXING
SOCKET SCREW
EYE BOLT
EYE LAG
U - BOLT

## Slide 12
ADDITIONAL TYPES OF FIXING
J - BOLTS
HANGER BOLTS
SHOULDER BOLT
ELEVATOR BOLT

## Slide 13
ADDITIONAL TYPES OF FIXING

## Slide 14: HEAD STYLES AND DRIVES
FLAT
OVAL
PAN
TRUSS

## Slide 15: HEAD STYLES AND DRIVES
ROUND
HEX
HEX WASHER
SLOTTED HEX WASHER

## Slide 16: HEAD STYLES AND DRIVES
SOCKET CAP
BUTTON

## Slide 17: HEAD STYLES AND DRIVES
PHILLIPS / FREARSON
SLOTTED
COMBINATION
SOCKET/ HEX/ ALLEN

## Slide 18: HEAD STYLES AND DRIVES
ONE WAY
SQUARE

## Slide 19
HEX
A six sided nut. Also referred to as a finished hex nut.
NYLON INSERT
A nut with a nylon insert to prevent backing off. Also referred to as a Nylock
LOCK / JAM
A hex nut with a reduced height.
NYLON INSERT LOCK / JAM
A Nylock nut with a reduced height..
WING
A nut with 'wings' for hand tightening
CAP
A nut with a domed top over the end of the fastener.
ACORN
Acorn nuts are a high crown type of cap nut, used for appearance.
FLANGE
A nut with a built in washer like flange.
TEE
A nut designed to be driven into wood to create a threaded hole.
SQUARE
A four sided nut.
PREVAILING TORQUE LOCK
A non-reversible lock nut used for high temperature applications
K-LOCK / KEP
A nut with an attached free-spinning external tooth lockwasher.
COUPLING
Coupling nuts are long nuts used to connect pieces of threaded rod or other male threaded fasteners..
SLOTTED
Slotted nuts are used in conjunction with a cotter pin on drilled shank fasteners to prevent loosening.
CASTLE
Castle nuts are similar to slotted nuts but with the slots in a rounded section above the main nut.
NUTS

## Slide 20: WASHER TYPES
FLAT
FENDER
FINISHING/CUP
SPLIT LOCK
WASHERS ARE ALL FRICTION LOCKING DEVICES!

## Slide 21: WASHER TYPES
EXTERNAL TOOTH LOCK
INTERNAL TOOTH LOCK
SQUARE
DOCK
WASHERS ARE ALL FRICTION LOCKING DEVICES!

## Slide 22: USING A TAB WASHER
WASHER BEGINS LIFE FLAT AND IS BENT INTO POSITION

## Slide 23: TAB WASHER FORMS
TAB WASHERS ARE ALL POSITIVE LOCKING DEVICES!

## Slide 24: THREE STEPS TO THREAD IDENTIFICATION
MEASURE THE
PITCH / T.P.I.
METRIC THREAD
NONE METRIC THREAD
STEP 01

## Slide 25: MEASURING THE PITCH
The pitch is the distance between thread peaks, or a similar position from one
thread to the adjacent thread.
EFFECTIVE DIAMETER

## Slide 26: MEASURING THE PITCH
2 mm

## Slide 27: MEASURING THE PITCH

## Slide 28: Measuring the TPI
Place the thread gauge onto the threads so it is flat, no light showing underneath.

## Slide 29: Measuring the TPI

## Slide 30: Refer the TPI to a thread chart
Diameter (Inches) | Threads Per Inch (TPI) |  |  | 
 | BSW | UNC | UNF | BSF
1/8 | 40 | 40 |  | 
5/32 | 32 | 32 |  | 
3/16 | 24 | 24 | 32 | 32
1/4 | 20 | 20 | 28 | 26
5/16 | 18 | 18 | 24 | 22
3/8 | 16 | 16 | 24 | 20
7/16 | 14 | 14 | 20 | 18
1/2 | 12 | 13 | 20 | 16
5/8 | 11 | 11 | 18 | 14
3/4 | 10 | 10 | 16 | 12
7/8 | 9 | 9 | 14 | 11
1 | 8 | 8 | 12 | 10
1-1/8 | 7 | 7 | 12 | 9
1-1/4 | 7 | 7 | 12 | 9
1-1/2 | 6 | 6 | 12 | 8

## Slide 31: THREE STEPS TO THREAD IDENTIFICATION
MEASURE THE
DIAMETER –
To next full size up!
THREE STEPS TO THREAD IDENTIFICATION
STEP 02

## Slide 32: Measure the diameter
Use a micrometer........

## Slide 33: Measure the diameter
Or use a vernier, so long as you understand how to read the measurement and you select the correct micrometer or vernier scale – mm / inches!

## Slide 34: Measure the diameter
General
There are several different locations on a fastener where one can measure the diameter.
The most commonly used diameters are:
Thread Diameter (T). Also called major diameter.
Shank Diameter (S). Also called the grip length.
Root Diameter (R). Also called minor diameter.

## Slide 36: THREE STEPS TO THREAD IDENTIFICATION
NOTE ANY
IDENTIFYING MARKS
STEP 03

## Slide 37: IDENTIFYING MARKS - BOLTS
CIRCULAR RECESSED
BOLTS
Three touching circles
IMPERIAL / UNIFIED THREAD

## Slide 38: IDENTIFYING MARKS - NUTS
FLAT HEAD BOLTS
– NO RECESS
THE LETTER “M” IS
EMBOSSED ONTO
THE SURFACE
METRIC THREAD

## Slide 39: IDENTIFYING MARKS - NUTS
CIRCULAR RECESSED
NUTS
PRECISION –
On the none bearing face
IMPERIAL / UNIFIED THREAD

## Slide 40: IDENTIFYING MARKS - NUTS
CIRCULAR RECESSED
NUTS
PRESSED–
On the none bearing face
IMPERIAL / UNIFIED THREAD

## Slide 41: IDENTIFYING MARKS - NUTS
Three touching rings for unified thread

## Slide 42: IDENTIFYING MARKS - STUDS
A “VEE” AND A LINE BELOW for unified thread

## Slide 43: IDENTIFYING MARKS – STUD HOLES
Three touching rings for unified thread,
stamped into the surface

## Slide 44: Identification Markings
Specs | Nominal Size (inch) | Proof Load Stress (ksi) | Tensile Strength (min ksi) | Material Notes
SAE Grade 1 | 1/4 to 1 1/2 | 33 | 60 | 1
SAE Grade 2 | 1/4 thru 3/4 | 55 | 74 | 
 | over 3/4 thru 1-1/2 | 33 | 60 | 
ASTM A307 | 1/4 to 1 1/2 | 33 | 60 | 3
SAE Grade 4 | 1/4 to 1 1/2 | 65 | 115 | 2,a
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered

## Slide 45: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
SAE - Grade 5 | 1/4 thru 1 | 85 | 120 | 2, b
ASTM A449 - Type 1 | 1 1/8 thru 1-1/2 | 74 | 105 | 
 | 1 3/4 thru 3 | 55 | 90 | 

## Slide 46: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
SAE - Grade 5.2 | 1/4 thru 1 | 85 | 120 | 4, b

## Slide 47: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
ASTM A325 - Type 1 | 1/2 thru 1 | 85 | 120 | 2, b
 | 1 1/8 to 1-1/2 | 74 | 105 | 

## Slide 48: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
ASTM A325 - Type 2 | 1/2 thru 1 | 85 | 120 | 4,b
 | 1 1/8 to 1-1/2 | 74 | 105 | 

## Slide 49: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
ASTM A325 - Type 3 | 1/2 thru 1 | 85 | 120 | 5,b
 | 1 1/8 to 1-1/2 | 74 | 105 | 

## Slide 50: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
ASTM A354 - Grade BC | 1/4 thru 2-1/2 | 105 | 125 | 5,b
 | 2-3/4 thru 4 | 95 | 115 | 

## Slide 51: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
SAE Grade 7 | 1/4 to 1 1/2 | 105 | 133 | 7,b

## Slide 52: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
SAE - Grade 8 | 1/4 thru 1-1/2 | 120 | 150 | 7,b
ASTM A354 - Grade BD | 1/4 thru 1-1/2 | 120 | 150 | 6,b

## Slide 53: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
SAE - Grade 8.2 | 1/4 thru 1 | 120 | 150 | 4,b

## Slide 54: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
ASTM A490 - Type 1 | ½ to1-1/2 | 120 | 150 | 6,b

## Slide 55: Identification Markings
Material Notes
Low or Medium Carbon Steel
Medium Carbon Steel
Low Carbon
Low Carbon Martensite
Weathering Steel
Alloy Steel
Medium Carbon Alloy
Treatment -
a - cold drawn b - quenched and tempered
ASTM A490 - Type 3 | 1/2 thru 1-1/2 | 120 | 150 | 5,b

## Slide 56: TAPPING A NEW HOLE
Step 1
Mark the location for the threaded hole with the ruler and scribe.
With the center punch and hammer, center mark the hole location.

## Slide 57: TAPPING A NEW HOLE
Step 2
Refer to the drill and tap chart to determine the correct size of the drill bit required for the tap. If the hole is larger than 1/2 an inch, you will need to drill a pilot hole before you can drill the final hole size. Do not use a pilot hole that is larger than 40 percent of the diameter of the final hole size. A larger pilot hole will cause the final drill bit to bind and break, resulting in a poor final hole quality or injury to the person drilling the hole.

## Slide 58: DRILL TO TAPPING CHART

## Slide 59: TAPPING A NEW HOLE
Step 3
Insert the drill bit into the drill. Apply cutting fluid to the center mark that you placed on the metal and onto the drill bit. Drill the hole through the metal, using steady pressure. Apply additional cutting fluid as necessary to keep the drill bit cool. If you are drilling into stainless steel, pump the trigger to keep the drill bit moving slow. Increased drilling speeds will result in your drill bit heating up and losing its cutting edge. With stainless steel, slower is always better.

## Slide 60: TAPPING A NEW HOLE
Step 4
Clean the shavings from around the drilled area with a clean rag. Insert the proper tap into the tee handle. A drill can be used to run the tap through the hole, but it is not recommended as even slight pressure other than straight down will break the fragile carbide tap.

## Slide 61: TAPPING A NEW HOLE
Step 5
Liberally coat the tap with cutting and tapping fluid. With the tap aligned straight with the hole, turn the tee handle clockwise to start tapping the hole. If you are tapping for left-handed threads, you need to turn the tee handle counter-clockwise for the tap to start in the hole.

## Slide 62: TAPPING A NEW HOLE
Step 6
Eliminate tap binding by turning the tee handle backwards 1/4 of a turn after each revolution of the tee handle. The 1/4 turn back will remove filing build-up from the front edge of the tap. Apply tapping fluid to the tap before continuing the tap into the hole.

## Slide 63: TAPPING A NEW HOLE
Step 7
Reverse the tap to remove it from the threaded hole. Remove the burr from the hole. Test the threads with the correct size bolt to ensure that the bolt threads correctly.

## Slide 64: TAPPING A NEW HOLE
The correct order of using the tap and wrench to cut a new thread is :-
S = STARTING tap
I = INTERMEDIATE tap
F = FINISHING tap

## Slide 65: TAPPING A NEW HOLE
The correct order of using the tap and wrench to cut a new thread is :-
T = Taper tap
I = INTERMEDIATE tap
P = PLUGGING tap
T I P

## Slide 66: INSERTING A STUD
All studs have an unthreaded portion between the two threaded ends.
Do NOT install studs using a pipe wrench on the unthreaded portion of the stud. Aside from possible damage to the threads, the marks or notches (Fig. 1) made by the pipe wrench create stress riser points in the stud.

## Slide 67: INSERTING A STUD
The accepted method for stud installation is as follows: (1) First thread Lock/Jam Nut into stud. (2) Place flat washer on top of Jam Nut. (3) Thread Full Nut onto stud over washer. (Assembly shown in Fig. 2) After assembly, stud may be driven into tapped hole In the casting using either impact wrench or hand wrench. The washer prevents turning of the nuts and reduces thread stresses.

## Slide 68: INSERTING A STUD
When installing new studs, care must be taken to assure that the stud Is not over-inserted. NEVER!! insert a stud into a tapped hole to the extent that it bottoms-out. If the stud is bottomed, the thread stresses are mislocated and the probability of stud failure is greatly increased.

## Slide 69: TAPPED HOLE OR STRAIGHT THROUGH

## Slide 70: ANTI-FRICTION COATING
AF coatings are dry lubricants consisting of suspensions of solid lubricants, such as graphite, PTFE or molybdenum disulphide of small particle size in a binder. Such coatings can be applied to fastener threads to replace metallic coatings such as zinc and cadmium and offer maintenance free permanent lubrication. By careful selection of the lubricants, AF coatings can be designed to meet specific applications. The coatings are permanently bonded to the metal surface and provide a lubricating film preventing direct metal to metal contact.

## Slide 71: BOLT
A bolt is the term used for a threaded fastener, with a head, designed to be used in conjunction with a nut.

## Slide 72: BOLT – ROOT DIAMETER
ACME THREAD

## Slide 73
ANY QUESTIONS